## Slide 1: Fission Research Overview
Benoit Forget
Associate Professor

## Slide 2: Fission Faculty
Thermohydraulic
Reactor Physics
Reactor Design
Energy Policy

## Slide 3
Fluoride-Salt-Cooled High-Temperature Reactor
  Fuel: TRISO particle fuel, no failure up to ~1650°C, strongly negative Doppler feedback
  GE Power Systems MS7001FB
Coolant: FLiBe liquid salt, low-pressure, chemically inert, large margin to boiling (1430C), high heat capacity, enables power density up to 10x gas-cooled reactors
Power Cycle: Modified natural-gas air Brayton power cycle with General Electric 7FB turbo-compressor
Drs. C. Forsberg, L. Hu

## Slide 4: Engineered surface nano- and micro-scale features (coatings, pores, posts, patterns, …) enhance CHF
Increases design-basis and beyond-design-basis safety margins and/or enables power uprates in LWRs
Profs. J. Buongiorno, M. Bucci
G=1000 kg/m2s, xe~0, SS316 surface

## Slide 5: High-fidelity Monte Carlo simulations
Focus on high performance computing in particle transport, improved physical models, and open source software for research and education
  On-the-fly Doppler Broadening
  Time-dependent Monte Carlo
  Multi-physics coupling
  Acceleration and convergence analysis
  Efficient parallelization algorithms
TREAT Reactor
Integration in multi-physics environment
Profs. B. Forget and K. Smith

## Slide 6: MIT Graphite Pile
Profs. K.Smith and B.Forget
25 MT of graphite
2.5 MT of natural uranium
Education
  Approach to critical
  Spatial flux distribution
  Rod worth
Research
  Validation of graphite S(a,b)
  Validation of high-fidelity simulation tools

## Slide 7: High-fidelity simulations of coolant flow in reactor core
Objective: High fidelity flow-thermal simulations of reactor cores
Challenge: Complex turbulence / computational requirements
Approach: STRUCTure-based hybrid turbulence modeling
Prof. E. Baglietto

## Slide 8: Testing and Modeling of Nuclear Fuels
  Objective: Improve Economics and Safety
    Impact of Fuels on System Level
  Experimental Effort (Steady & Accidents):
    Fuel Cladding: Zirc-4, Coatings, SiC Composites
    Fuel Pellet: UO2, UN
    Unique High Temperature (up to 2000 oC) & High Pressure Testing Capability
  Simulation Effort (Steady & Accidents):
    Reactor Physics Analysis (Application)
      Proven/Commercial Tools - STUDSVIK
    Thermal Hydraulics Development and Analysis
      Advanced Simulation Tools - TRACE
    Structural Mechanics Development and Analysis
      High Fidelity Tools – MOOSE/BISON
Prof. Shirvan

## Slide 9: Improving Economics of Reactors
  Objective: Acceleration of Innovative Technology R&D to Reduce Nuclear Cost
  Projects Focus on Design and Economics Modeling with Uncertainty for Advanced Reactors (including light water SMRs and power cycles)
    Sponsored by ARPA-E, DOE, EDF, TEPCO
Prof. Shirvan
Chart: Generation Capacity (GW)
| 2015 | 2018.38709677419 | 2019.9395161290299 | 2028.5483870967701 | 2030.10080645161 | 2031.3004032258 | 2032.5705645161199 | 2033.3467741935401 | 2035.2520161290299 | 2036.38104838709 | 2037.15725806451 | 2038.4979838709601 | 2040.0504032258 | 2041.25 | 2043.15524193548 | 2046.33064516129 | 2047.9536290322501 | 2049.9294354838698 | 2052.1169354838698 | 2052.96370967741 | 2055.15120967741 | 2055.8568548387002 | 2075
60-year | 98.1846 | 98.1626 | 96.3389 | 96.0163 | 93.6747 | 91.3357 | 84.0771 | 82.0002 | 65.9343 | 63.0781 | 57.8944 | 54.7776 | 52.9539 | 48.0259 | 44.905 | 20.5449 | 8.1058 | 1.6186 | 1.8614 | 0.3017 | 0 | 0 | 0
80-year | 98.1846 | 98.1626 | 96.3389 | 96.0163 | 94.1831 | 91.3274 | 89.7609 | 84.8335 | 81.1818 | 81.4302 | 80.6483 | 80.5883 | 77.4742 | 76.1729 | 73.0588 | 70.7214 | 62.9476 | 59.573 | 58.2723 | 53.3464 | 52.0456 | 52.0367 | 46.5858 | 45.5423 | 43.4633 | 20.1404 | 6.6641 | 1.472 | 1.7147 | 0.41393 | 0.39722

## Slide 10: MIT Nuclear Reactor Laboratory
6 MW light water reactor
  HEU fuel
Education
  Student operators
  Lab experiments using beam ports
Research
  LEU conversion
  FHR salt-irradiation
  Accident tolerant fuels and cladding
  Beam optics
Drs. Hu, Kohse, Sun, Carpenter, Moncton, Khaykovich…