## Slide 1: Nuclear Disarmament Verification via Resonant Phenomena (and other adventures in nuclear security) Areg Danagoulian

## Slide 2: Outline
What’s the big problem? (Nuclear Arms Reduction Treaties)
Why template verification and how does it work?
What is Nuclear Resonance Fluorescence (NRF)?
   NRF based verification
Epithermal neutron physics
   epithermal neutron verification

## Slide 3: Nuclear Arsenals
Significant Reduction since the Cold War
,, Доверяй, но проверяй! ’’ Но как? How? Ինչպե՞ս:

## Slide 4
How do treaty partners verify that the other side is dismantling actual warheads and not fakes? They don’t.
Verification: delivery vehicles – easier to verify.
Problems: large leftover of non-deployed warheads
  theft  nuclear terrorism, nuclear proliferation
 Authenticate warheads, without revealing secret information
VERIFICATION

## Slide 6
Previous Research:
information barriers, attribute verification
Developed at US national labs and AWE (UK)
Electronic Information Barrier – perform measurements, light up red/green lights. No direct access to classified data.
Verify the attributes of a weapon:
  is there plutonium inside? ✔
  High-Explosives present? ✔
  etc. ✔
 risk of diversions/spoofing
Has long ears?
Has big feet?
Has furry tail?
Has long ears?
Has big feet?
Has furry tail?
The info. barriers are in electronics/software  backdoors, hacks, software exploits
 risk of information leakage

## Slide 7
Authenticated template
“golden copy” of W88
Picked from a randomly
selected ICBM
Our Research:
physics-based cryptography, template verification
Candidate
copies, W88
. . .
Is A0 = A1 ?
A0 = A2 ?
A0 = A3 ?
. . .
To dismantlement
Challenge: perform
checks while
protecting secrets
isotopicaly sensitive
need a physical cryptography
need resonances!
A0
A1
A2
A3

## Slide 8: Analogy: NRF to Optical Spectroscopy
Optical Spectroscopy
Nuclear Spectroscopy
Bremsstrahlung
Back-scattered NRF
Transmitted NRF
Absorption lines, ~eV
NRF: unique fingerprint of isotopics
(W. Bertozzi)

## Slide 9: Broad-spectrum source  NRF
1733 keV
0
U-235
46 keV
1769 keV
1815 keV
unique line spectra for U-235, U-238, Pu-239, Pu-240…
detector
U-235 NRF spectrum
Γ ~ meV  thermal motion  eV

## Slide 10: NRF Weapon authentication Concept
Bremsstrahlung
(X-ray)
HPGe
Shielding
Cryptographic Foil
Everything classified by the host
Everything open
NRF filtered brem
Hosts:
provide the candidate warheads (to be authenticated)
Foil – thickness unknown to the inspectors, but of agreed upon isotopes
Inspectors:
Detector, electronics (to be verified by hosts)
Visual access to the foil
Joint:
Template (“golden copy”)

## Slide 11: NRF Weapon authentication Concept
A
B
HPGe
Shielding
Weapon A: authenticated template
Everything classified by the host
Physical Cryptography:
  No direct data from the weapon itself
  SIGNAL =
  Impossible to extract (Weapon)
Soundness and completeness:
  Authenticated template A -- acquire SNRF(A)
  Candidate weapon B -- acquire SNRF(B) and compare
Weapon B: candidate
Everything open
Bremsstrahlung
(X-ray)
NRF filtered brem
Cryptographic Foil
Notes: Mention that Brian Quitter and

## Slide 12
Simulated 2.1 or 2.5 MeV bremsstrahlung beam
> 1000 core hours for sufficient NRF statistics

## Slide 13
Genuine template
U-238 hoax
(J. Vavrek)

## Slide 14: Canonical hoax scenarios
Hoax scenario | Strongest discrepancy (σ)
WGPu  U-238 | 107
WGPu  FGPu | 14.6
R.S. Kemp, A. Danagoulian, R. Macdonald, J.Vavrek, Physical cryptographic verification of nuclear warheads, PNAS 113 (2016) 31.
Notes: We are sensitive to isotopics enough that we can easily detect slight changes from WGPu to RGPu. Sigma standard deviation
We pick the direction randomly

## Slide 15: NRF experimental setup
photon beam axis
HPGE
g detector
x-ray
imager
DU target
Cu radiator
-e, 2.5MeV
Vacuum Tubes!!!
Van de Graaff Accelerator
2.5 MeV e-, DC beam
20 mA

## Slide 16: Proxy Warhead
3mm of 238U
0.5mm of 27Al
1.5” of plastic
“MIT Linear Implosion Design”

## Slide 17: Experimental setup

## Slide 18: Hoax to Genuine comparisons
-- Lead Hoax
-- genuine
“Perfect Hoax”
Target:
Plastic “explosive”
Uranium
Al

## Slide 19: Hoax to Genuine comparisons
Target:
Plastic “explosive”
3mm Uranium
Al
Pb
8σ discrepancy in U lines
identical counts in Al
238U
27Al
(J. Vavrek)

## Slide 20: Hoax to Genuine comparisons
Target:
Plastic “explosive”
6mm Uranium
Al
Pb
11σ discrepancy in U lines
identical counts in Al
27Al
238U
Half hoax discrepancy: 5σ
Full hoax discrepancy: 11σ

## Slide 21: Extrapolations: the real bomb
5-10 σ in a (1+1)-hour proof-of-concept
“Black Sea” model:
6X rate decrease
25 uA  2.5 mA beam current:
100x rate increase
3  30 HPGe detectors:
10x rate increase
measurement times of ~minutes
IBA TT100 Rhodotron
Black Sea Model
GammaSphere
2m
J. R. Vavrek, B. S. Henderson, A. Danagoulian, “Experimental demonstration of an isotope-sensitive warhead verification technique using nuclear resonance fluorescence,” PNAS (2018), 201721278; DOI: 10.1073/pnas.1721278115

## Slide 22
Furthermore: validation of NRF models and cross sections
Multiple additional diagnostics from verification measurements:
  Accelerator current readout
  Downbeam bremsstrahlung flux monitor (LaBr3)
  Systematics across different:
    Detectors
    Energies
    Proxy warheads
Can use verification data to make absolute NRF cross section measurements!

## Slide 23
Results
NRF line | Avg model/obs ratio
U-238 2.176 MeV | 1.20 ± 0.02
U-238 2.245 MeV | 1.14 ± 0.03
Al-27 2.212 MeV | 1.06 ± 0.02
Model # | Avg model/obs ratio
Model 0 | 1.13 ± 0.01
Model 1 | 1.10 ± 0.01
Model 2 | 1.10 ± 0.01
Model 3 | 1.12 ± 0.01
Ratios of absolute NRF count rates, model over data:
Average: 1.11 ± 0.01 (stat)
More Geant4-reliant
Modest added benefit
>10% variation in literature values for NRF cross sections
Systematic uncertainty analysis ongoing
Model inversion to extract cross sections ongoing

## Slide 24
Verification with Epithermal Resonant Assay
(VERA)

## Slide 25: Epithermal Resonant Cryptographic Radiography
Epithermal neutron resonances in the 1-10 eV
Transmitted spectrum = isotopics geometry.
cryptographic reciprocal mask
~ flat image: no geom. information
spectrum reveals nothing about the pit
(TOF)
cryptographic

## Slide 26: Simulations: Geometric hoax resistance
template
hoax
(J. Hecla)

## Slide 27: Simulations: WGPu pit vs. a RGPu hoax
+ Different isotopics result in
different transmission
spectra
+ Only ~100k incident counts necessary for a 5σ detection

## Slide 28: Geometric Information Security
+ Compare the transmission image of the pit+reciprocal to that of a flat plate of the
same total thickness
+ Images and spectra are identical – can’t differentiate, thus cannot infer any geometric
information  geometric Zero Knowledge!
pit+reciprocal plate radial comparison

## Slide 29: Isotopic Information Security
+ Protect the isotopics of the pit.
+ isotopics(pit+reciprocal) ≠ isotopics (pit)
+ MC simulations of three scenarios:
- 70% 239Pu enriched pit, 98% enriched extension
- 78% enriched pit and extension
- 93% pit, 71% extension
- the transmitted spectra are identical
 isotopic Zero Knowledge
Jake J. Hecla, Areg Danagoulian, “Nuclear Disarmament Verification via Resonant
Phenomena,” Nature Communications 9, 2041-1723 (2018)
Jake’s MIT undergrad thesis

## Slide 30: The Future
Perform epithermal experiments at LANL to prove the concept
Collaborate
  national labs
  other countries
  Russia
Need technological solutions for treaty verification  more ambitious, far reaching treaties

## Slide 31
Dr. Brian Henderson
Students:
Jimmy Jayson Julie Bobby Jeremiah Ezra Ben
The Team
PhD
S.M.
Undergraduate
Postdoc:
Alumni:
Jake Hecla Dr. COL Buck O’Day Jill Rahon

## Slide 32: BACKUP

## Slide 33: Experimental setup
Brems
NRF
~2.6 MeV e-
Radiator
(Cu + Au)
Warhead proxy
Encrypting foil
(DU + Al)
Genuine: DU + plastic
Hoax: Pb + plastic
HPGe
LYSO, LaBr downbeam