## Slide 1: Rocketry Basics
MIT Rocket Team
Jamie Abel
Original Course by Andrew Reilley

## Slide 2: Your 1st High-Powered Rocket

## Slide 3: L1 Certification
Permission from the National Association of Rocketry (or Tripoli) to use motors above a certain size at sanctioned launches.
Requirements:
Be familiar with your own rocket and how it works
Safe flight
  Doesn’t break
  Stable flight
  Recovery
Motor
  H or I impulse
  T/W > 5, ideally
Notes: Motor, stability, recovery. How do we do all of those things? Many ways possible, here’s one that we’re going to build

## Slide 4: A basic rocket

## Slide 5: A basic rocket
Forward
Aft
3”
~4’

## Slide 6: A basic rocket
Nosecone
Body Tube
Fins

## Slide 7: A basic rocket
Recovery System
Motor Mount
Centering Ring

## Slide 8: Basic Rocket Flight
Stable boost
Safe recovery
Separation

## Slide 9: Structure - Nosecone
Shoulder
Notes: Typically plastic

## Slide 10: Structure - Fins
Root
Leading edge
Tip
Trailing edge

## Slide 11: Purpose of Fins - Stability

## Slide 12
Unstable

## Slide 13
Stable

## Slide 14: Stability Margin
Center of Mass
Center of Pressure
Without Fins - Unstable
With Fins - Stable
Static Margin
Notes: Aim for around 1.5 cal of stability (+- 0.3)

## Slide 15: Attaching Fins
Tab

## Slide 16: Recovery System Parts
Parachute
Parachute protector
Shock cord

## Slide 17: Recovery System Deployment
Motor
Motor
Black Powder Charge
Para-chute
Protector

## Slide 18: Recovery System
Parachute
Shock cord
Notes: Typically about 12 feet of ¼” kevlar for the SC, a 24-30 inch nylon chute.

## Slide 19: Recovery System Attachment
Threaded through holes in nose cone shoulder. Don’t use the built-in attachment point!
Passed through notch in centering ring glued to motor mount
Notes: They love to ask this one during L1 checkins. Note: don’t use the built in nosecone eyelet. It is tempting, but they break really easily.

## Slide 20: Motor
L1: Must use an H or I motor (160 - 640 NS)
Thrust ring

## Slide 21: Motor Mount
Centering rings
Motor mount tube

## Slide 22: Motor Retention
Screw threaded into nut on forward side of CR
Clip that prevents motor from leaving MMT
Motor thrust ring seats directly on MMT

## Slide 23: Launching - Rail Buttons

## Slide 24: Questions?

## Slide 25: Next – OpenRocket