## Slide 1: Challenges on ASTRO-H Calibration Plans
“Bish” K. Ishibashi (Nagoya U.)
R. Petre (NASA’s Goddard)
J.-W. den Herder (SRON)

## Slide 2: ASTRO-H Calibration Advisory Board
Calibration Advisory Board is established for ASTRO-H in order to help facilitate complex calibration plans which are to be executed in proper and efficient manner by instrument teams.
Three of us are appointed to serve for the purpose.
Software / Calibration Team (SCT led by Terada and Angelini) is established for the same concept.
Unofficial Remark: We are here to make the lives of instrument teams easier by providing advices on calibration when and where needed (on occasion, provide hard, physical labor…[ Bish]).

## Slide 3: ASTRO-H Calibration Plans
Having four instruments covering the energy range from 0.3 ~ 600keV, it is imperative for ASTRO-H to have good cross-calibration plans among instruments, as well as good calibration goals for each instrument.
We are here at this IACHEC to “give” you excellent opportunities to provide us insights on what you might do (differently) if you are to plan calibration activities for ASTRO-H.

## Slide 4: ASTRO-H Calibration Plans
How accurately can we
cross-calibrate between
SXI-SXS-HXI-SGD?
What actions are needed on
ground and in flight to ensure
high accuracies of calibration
in the overlap region?

## Slide 5: ASTRO-H Calibration Plan
Graphic Representation
of
ASTRO-H Calibration Plans

## Slide 6: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Line Profile
Gain Stability /
Thermal Variations
NXB
Stray Light
Instrumental noise
Contamination
Filters
Thermal Shields
On-Axis PSF
Off-Axis PSF
PSF core (r < 20”)
PSF wing (r > 20”)
Vignette
On-Axis EA
Off-Axis EA
To list a few examples
of cal items..

## Slide 7: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
On-Axis PSF
Off-Axis PSF
PSF core (r < 20”)
PSF wing (r > 20”)
Vignette
On-Axis EA
Off-Axis EA
NASA/GSFC 100m diverging beam facility used
Measurement at E = 1.5, 4.5, 8.0, and 9.4 keV (proposed based on the Suzaku lessons)
1G-effect, imperfection in geometry/alignment examined (incl. the effect of vibration test)
EM test planned in April / June 2011
Expected accuracies in 5 – 10 %
Science requirement ~ 3 % (the goal not met)
For Effective Area & PSF Cal…

## Slide 8: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Detector Response
Background
On-Axis PSF
Off-Axis PSF
PSF core (r < 20”)
PSF wing (r > 20”)
Vignette
On-Axis EA
Off-Axis EA
NASA/GSFC 100m diverging beam facility used
for the PSF core
ISAS/JAXA 30m pencil beam facility used
for the PSF tail/wing
Measurement at E = 1.5, 4.5, 8.0, and 9.4 keV (proposed based on the Suzaku lessons)
Vignetting – planned w/o specifics
FM test planned in Feb. / Sept. 2012
Expected accuracies in a few %?
Science requirement ~ 3 % (the goal not met)
Transmission
For Effective Area & PSF Cal…

## Slide 9: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Detector Response
Background
Contamination
Filters
Thermal Shields
Transmission
SPring-8 BL25SU measurement conducted
C-K, N-K, O-K, Al-K edges sampled at 0.2eV
(see example at Al-K below); in 0.8 – 1.8keV
at 10eV; otherwise (in 0.12 – 1.8keV) at 5 eV
Measured accuracies: better than 1% in general
Brookhaven/NSLS facility & LLNL/EBIT used
  for filter transmission
Thickness verification & edge structure examined
EM test in Apr 2011; FM test in Nov 2011
Expected accuracies: < 5%
Uncertainty in transmission would affect that of EA.

## Slide 10: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Line Profile
Gain Stability /
Thermal Variations
Eckart et al. 2011
NASA/GSFC facility used
QE = Absorber weight / area
Uncertainty in QE < 1 %
Mission Requirement: < 5 %

## Slide 11: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Line Profile
Gain Stability /
Thermal Variations
Eckart et al. 2011
NASA/GSFC facility used
σFWHM ~ +/-1eV (Goal 0.2eV)
Gaussianity of profile expected
Spectral redistribution
Measure several energies in
EM integration in May 2011
Science Requirement: < 1.6eV

## Slide 12: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Line Profile
Gain Stability /
Thermal Variations
Kelley et al. 2011

## Slide 13: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Line Profile
Gain Stability /
Thermal Variations
NASA/GSFC facility used (ISAS in later EM test)
ΔE ~ +/-2eV (Goal 0.5 – 1 eV)
Measure several energies in EM integration test in May / June 2011
FM test planned in the same manner; more extensive in large matrix of operating conditions
Use of Modulated X-ray Sources (MXS) in flight
Science Requirement: 0.5 – 1 eV (marginally OK)

## Slide 14: ASTRO-H: SXT – SXS Calibration Items
SXT-SXS
Effective Area
PSF
Transmission
Detector Response
Background
NXB
Stray Light
Instrumental noise
To be furnished later.

## Slide 15: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Resolution
Energy Response
Gain Stability
NXB
Stray Light
Instrumental noise
Contamination
Entrance Window
Thermal Shields
On-Axis PSF
Off-Axis PSF
Vignette
On-Axis EA
Off-Axis EA
To list a few examples
of cal items..
PC
Pb sheet
Veto: BGO/APD

## Slide 16: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
On-Axis PSF
Off-Axis PSF
Vignette
On-Axis EA
Off-Axis EA
SPring-8 BL20B2 facility used for calibration
Without Pre-Collimator
  EA Measurement at E = 8(?), 30, 70 keV (TBD)
  Vignetting – 8 offset + nominal
With PC (prior to vibration test)
  EA Measurement at E = 30keV only (TBD)
  No vignetting
With PC (after vibration test)
  EA Measurement at E = 30keV only (TBD)
  Vignetting – 8 offset + nominal
1kev Step beam data needed (EPR rec.) but feasible?
Expected accuracies in 5 – 10 % (TBD in flight)
Science requirement ~ 5 % (marginal)
Transmission
For Effective Area & PSF Cal…

## Slide 17: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
On-Axis PSF
Off-Axis PSF
Vignette
On-Axis EA
Off-Axis EA
Transmission
For Effective Area & PSF Cal…
Preliminary Result
From SPring-8:
Partial Raster Scan
at 30 keV.

## Slide 18: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
On-Axis PSF
Off-Axis PSF
Vignette
On-Axis EA
Off-Axis EA
Transmission
For Effective Area & PSF Cal…
Question to everyone:
At what high/low energies should we calibrate
the HXT’s effective area? What factor should
determine our choices? Science-based ideas (use
of a continuous spectrum)? Or crucial calibration
band that we need to have a well refined EA cal?

## Slide 19: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
For thermal shield (by Toh-Ray):
Proposals in for utilizing SPring-8 BL25SU and/or KEK/PF
Possibly done in post-flight with the same sample?
For entrance window:
  TBD (polycarbonate used in EM; evapolated Al in FM)
Uncertainties here need to be accounted in EA
Transmission
Contamination
Entrance Window
Thermal Shields
Optical Constant for Pt edges needed
GEANT4 data needed as well

## Slide 20: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
Transmission
QE/QEU
Energy Resolution
Energy Response
Gain Stability
ISAS/JAXA facility used
Uncertainty in QE: TBD
Science Requirement in EA: 5 %

## Slide 21: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
Transmission
QE/QEU
Energy Resolution
Energy Response
Gain Stability
ISAS/JAXA facility used
EFWHM at 60keV:
  Si ~ 1.1 keV
  CdTe ~ 1.4 (Al) & 1.3 (Pt) keV
Science Requirement: ~ 1keV?
Kokubun et al. 2011

## Slide 22: ASTRO-H: HXT – HXI Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
Transmission
QE/QEU
Energy Resolution
Energy Response
Gain Stability
ISAS/JAXA facility used
Test Pulse Injector in ASIC to monitor gain variations in the HXI-DE
Uncertainty in gain: TBD
Science Requirement: 3 %? (seems poor)

## Slide 23: ASTRO-H: Calibration Items
HXT-HXI
Effective Area
PSF
Detector Response
Background
Transmission
To be furnished later.

## Slide 24: ASTRO-H: Calibration Items
SGD
Effective Area
Vignette
Transmission
Detector Response
Background
QE/QEU
Energy Response
Gain Stability
NXB
Stray Light
Instrumental noise
Contamination
Entrance Window
Off-Axis PSF
On-Axis EA
Veto: BGO/APD
Modes

## Slide 25: ASTRO-H: Calibration Items
SGD
Effective Area
Vignette
Transmission
Detector Response
Background
QE/QEU
Energy Response
Gain Stability
Contamination
Entrance Window
On-Axis EA
Modes
36864 channels to be calibrated
  Each detector pad to be calibrated separately with radioactive sources (241Am,57Co, 22Na, 137Cs).
  line channel checked for each pixel to correct for gain
  line strength checked for effective EA (+ QE).
  Can be done at any site with radioactive sources, clean room, etc.
The whole 36864 channels after integration
  Ditto as above, but with difficulties in reduction of flux by fine-collimator…
Test pulse injection in ASIC used for gain correction in electronics.

## Slide 26: ASTRO-H: Calibration Items
SGD
Effective Area
Vignette
Transmission
Detector Response
Background
Off-Axis PSF
Fine Collimator (BBM)
Fine Collimator
  Structural measurements (distortion, gap / shift in welding points, etc)
  Precise 3-D info to be fed into GEANT4 model

## Slide 27: ASTRO-H: Calibration Items
SXT-SXI
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Response
Operation Modes
NXB
Stray Light
Instrumental noise
Contamination
Blocking Filters
Thermal Shields
On-Axis PSF
Off-Axis PSF
PSF core (r < 20”)
PSF wing (r > 20”)
Vignette
On-Axis EA
Off-Axis EA

## Slide 28: ASTRO-H: Calibration Items
SXT-SXI
Effective Area
PSF
Transmission
Detector Response
Background
QE/QEU
Energy Response
Operation Modes
What modes can be made available and how well will they be calibrated prior to or in flight.
Can we selectively turn off CCD chips not needed?

## Slide 29: ASTRO-H Calibration Plan
This page is left unintentionally blank. Oops.